## Slide 1
SAP1-Plus Ultra

## Slide 2
Group:- G7
Team:-
Ibrahim Samy Section 1
Yahia Mohammed Section 4
Yahia Shaban Section 4
Youssef Samy Section 4

## Slide 3
Youssef Samy

## Slide 4
SAP-1 is the first stage in the evolution towards modern computers.
The main purpose of SAP is to introduce all the crucial ideas behind computer operations.
Being a simple computer, SAP-1 also covers many advanced concepts.
SAP-1 is a bus organized computer. All registers are connected to the W bus with the help of tri-state buffers.

## Slide 5
Simple-As-Possible.
One output device with 8 LEDs
32 bytes of Memory.
7 instructions
  3 with 1 operand
  4 with no operand.
Accumulator Architecture
  Accumulator
  Out Register
  B Register
  Word size 8-bit
5
5
5
5
5
3
2-bit
ALU
MAR

## Slide 6
Architecture
8-bit "W" bus.
5-bit program counter, only counts up, it
starts counting from 0 and counts up to 31.
5-bit Memory Address Register (MAR).
32 Byte Memory.
8-bit (1 Byte) Instruction Register (IR).
5-cycle controller with 13-bit
control signal
8-bit Accumulator.
8-bit B Register.
8-bit ALU.
8-bit Output Register.

## Slide 7
Processor Updating
How to make the SAP-1 Better

## Slide 8
Goals
RAM Size
Make the RAM Bigger
01
ISA
Add More Instructions
02
Execute Time
Decrease The execution time
03
ADDER/SUBTRACTOR
Add more functionality
04

## Slide 9
Old vs New (Instruction)
Old
New
The instruction consists of 8bits:
Divided to:
4 bits address
4 bits opcode
Instruction
The instruction consists of 8bits:
Divided to:
5 bits address
3 bits opcode
Instruction
0
4
5
7
Opcode
Address of Operand
0
3
4
7
Opcode
Address of Operand

## Slide 10
Result
Version | Accessible Locations | Max No of Instructions
Old | 24 = 16 | 24 = 16
New | 25 = 32 | 23 = 8
The #instructions has decreased but still sufficient

## Slide 11
Old vs New (ALU)
Old
New
It can only do some arithmetic operations such that ADD & SUB
ADDER/SUBTRACTOR
By adding some logical operations such that Logical Shift Right & Shift left
It has become an ALU
ALU

## Slide 12
Result
ADD/SUB
ALU
Logical Shift Right Operation Hardware
Logical Shift Left Operation Hardware
Multiply Operation Software
Division Operation Software

## Slide 13
Old vs New (Controller)
Old
New
Any Instruction Takes 6 time signals to be executed
  3 time signals for fetch
  3 time signals for execute
Instruction Execute Time
Make the fetch takes only 2 time signals
Reset the signal counter immediately after the instruction execution finish
Instruction Execute Time

## Slide 14
Result
Make the Processor Faster
Less Power Consumption

## Slide 15
Yahia Mohamed

## Slide 16
Blocks

## Slide 17
SAP-1 uses a 2's complement adder-subtractor. When input Su is (logic 00), the sum is:
S = A + B
When Su is (logic 10), Shift left is:
S = A << 1
The ALU is asynchronous and its contents change as soon as the input changes
When EU is high, these contents appear on the W bus.
ALU
When Su is (logic 01), the Shift Right is:
S = A >> 1
When Su is (logic 11), the sub is:
S = A + B’ + 1
ALU
8
8
S
u
E
u
8

## Slide 18
To add/sub/shift two 8-bit numbers A and B, the accumulator register stored the number A.
The Accumulator has two outputs.
  One output goes to the ALU
  The other goes to the bus through tri-state buffers.
It also stores the (answer of two values) output of ALU through w-bus, when L is low.
It’s value is appeared on w-bus when E is high, which can then be read by output register.
A
Accumulator
Accumulator
8
8
L
A
CLK
E
A
A
8

## Slide 19
To add/sub/ shift two 8-bit numbers A and B, the B register stored the number B.
It supplies the number to be added or subtracted from the contents of accumulator to the ALU.
When data is available at W-bus and L goes low, at the rising clock edge, B register loads that data.
B Register
B Register
8
L
B
CLK
8
B

## Slide 20
Yahia Shaban

## Slide 21
Program counter
Program counter
5
C
p
CLK
E
P
CLR
When SAP-1 is Running Mode )Cp is active), the (5-bit) address is generated by the Program Counter which is then stored into the MAR through W bus (Ep is active).
The MAR stores the (5-bit) address of data and instruction which are placed in memory.
A bit later, the MAR applies this 5-bit address to the RAM, where Data or instruction is read from RAM

## Slide 22
MAR
MAR
5
5
LM
The MAR stores the (5-bit) address of data and instruction which are placed in memory.
When SAP-1 is Running Mode, the (5-bit) address is generated by the Program Counter which is then stored into the MAR through W bus.
A bit later, the MAR applies this 5-bit address to the RAM, where Data or instruction is read from RAM.

## Slide 23
RAM
32*8
8
CE
Memory
In initial design, the RAM is a 32 x 8 static TTL RAM. It means there are 32 memory locations (from 0 to 31) and each location contains an 8-bit of data/instruction.
You can program the RAM to be used for address and data. This allows you to store a program and data in the memory before a computer run.
During a computer run, the RAM receives 5-bit addresses from the MAR and a read operation is performed,
in this way, the instruction or data stored in the RAM and when is low the data placed on the W bus for use in some other part of the computer.
5
CE

## Slide 24
Instruction Register
Instruction Register
8
5
3
LI
EI
When the instruction is placed at bus from memory, the Instruction Register stores this instruction on the next rising clock edge.
The contents of the instruction register are split into two parts.
The upper part (3-bit) is a two-state output that goes directly to the block labeled "Controller-sequencer“
The lower part (5-bit) is a three-state output that is read onto the bus when is low
EI

## Slide 25
At the end of an arithmetic operation the accumulator contains the word representing the answer.
Then answer stored in the accumulator register is then loaded into the output register through W-bus.
This is done in the next positive clock edge when EA is high and LO is low.
Output Register
Output Register
Lo

## Slide 26
Yahia Mohamed

## Slide 27
The Control Unit is responsible for linking all the components together
Then it executes the Instruction using 13-bits different Control Signals
Controller
The Controller receives 3-bit opcode from IR register
Controller / Sequencer
3
13
Opcode
Control Signals
Control Signals :-
    CP EP LM CE LI EI LA EA SU(2bits) EU LB LO

## Slide 28
Control Signals
Controller / Sequencer
CP
EP
LM
CE
LI
LA
EA
SU
EU
LB
LO
Signal | Size | Active | Function
CP | 1 bit | High | Increase the PC
EP | 1 bit | High | Write PC content on BUS
LM | 1 bit | Low | Load MAR from BUS
CE | 1 bit | Low | Write RAM content on BUS
LI | 1 bit | Low | Load IR from BUS
EI | 1 bit | Low | Write IR content on BUS
LA | 1 bit | Low | Load ACC from BUS
EA | 1 bit | High | Write ACC content on BUS
SU | 2 bits | N/A | Select ALU operation
EU | 1 bit | High | Write ALU content on BUS
LB | 1 bit | Low | Load Register B from BUS
LO | 1 bit | Low | Load OUT Register from BUS
EI

## Slide 29
Ibrahim Samy

## Slide 30
Instruction Set
LDA
opcode
000 ADDRESS
ACMEM[MAR]
SUB
opcode
010 ADDRESS
AC  AC-B
ADD
opcode
001 ADDRESS
ACAC+B
SHIFT LEFT
011 XXXX
AC sll AC
SHIFT RIGHT
opcode
100 XXXX
AC  srl AC
HLT
opcode
111 XXXX
CLK0
OUT
opcode
101 XXXX
OUTAC
0
4
5
7
Opcode
Address of Operand

## Slide 31
Instruction cycle
Fetch instruction
Execute the instruction
Decode instruction

## Slide 32
Fetch
T1,T2
During the memory state, CE' and L'I are active. The addressed RAM word sets up the instruction register via the W bus. Midway through the memory state, a positive clock edge loads the instruction register with the addressed RAM word.
IRM[AR]
This sets up the program counter to count positive clock edges. Halfway through the increment state, a positive clock edge hits the program counter and advances the count by 1.
During the increment state, CP ,Li is the only active control bits.
PCPC+1
IRM[AR]
The address, increment, and memory states are called the fetch cycle of SAP-l.
During the address state, EP and LM are active; this means that the program counter sets up the MAR via the W bus.
A positive clock edge occurs midway through the address state; this loads the MAR with the contents of the PC.
ARPC

## Slide 33
Execution Cycle :
The next three states (T3, T4, and T5) are the execution cycle of SAP-1
The register transfers during the execution cycle depend on the particular instruction being executed.
What follows are the control routines for different SAP-1 instructions.

## Slide 34
Macro Instructions :
The instructions we have been programming with (LDA, ADD, SUB, . . .) are sometimes called macro-instructions to distinguish them from micro-instructions.
Each SAP-1 macroinstruction is made up of maximum three micro-operations. For example, the LDA macroinstruction consists of the two micro-operations.

## Slide 35
Micro operation :
The controller-sequencer sends out control words, on during each T state or clock cycle.
These words are like directions telling the rest of the computer what to do.
Because it produces a small step in the data processing, each control word is called a micro-operation.

## Slide 36
Youssef Samy

## Slide 37
Ex:1
instruction
Data in memory

## Slide 38
Ex:2
instruction
Data in memory

## Slide 39
Thanks' for your time